## Slide 1: RTOS architecture (Rate Monotic Scheduler with pre-emption)
Rate_Monotonic_Scheduler
Inner_Loop_Thread (2.5ms)
Data_Acquistion_Task
FDIR_Task
Attitude_Controller_Task
Priority
1
Outer_Loop_Thread (20ms)
Mission_Manager_Task
Position_Controller_Task
Priority
2
Telemetry_Thread (aperiodic)
FDIR_Task_Notify
Logger
Priority
3
Interrupt_Service_Routine
Hardware Preemption
Hardware_Timer
Deadline_Monitor (WDT)
Hardware_IO Ports

## Slide 2: Inter-Process Communication
Task | Data | Read/Write | Mechanism
Data_Acquisition_Task | IMU_Rate Heading GPS Altitude Airspeed Sensor_Mode Sensor_State Target_Altitude Manual_Commands | Read | Priority-Inheritance Mutex
FDIR_Task | FDIR_Health Number_Of_Failures | Write | Priority-Inheritance Mutex
Attitude_Controller_Task | IMU_Rate Kin_State_Correction Roll_Target Pitch_Target Yaw_Target Throttle_Target Autopilot_Mode Flight_Phase | Read | Priority-Inheritance Mutex

## Slide 3
Task | Data | Read/Write | Mechanism
Attitude_Controller_Task | Predicted_State Elevator_Saturation Aileron_Saturation Rudder_Saturation ESC_Saturation Predicted_State | Write | Priority-Inheritance Mutex/Double-Buffering for Predicted_State
Mission_Manager_Task | Pilot_Action Target_Alt FDIR_Health Predicted_State Number_Of_Failures | Read | Priority-Inheritance Mutex/Double-Buffering for Predicted_State
Mission_Manager_Task | Autopilot_Mode Flight_Phase | Write | Priority-Inheritance Mutex
Position_Controller_Task | Heading GPS Altitude Airspeed Predicted_State FDIR_Health | Read | Priority-Inheritance Mutex/Double-Buffering for Predicted_State
Position_Controller_Task | Roll_Target Pitch_Target Yaw_Target Throttle_Target | Write | Priority-Inheritance Mutex